Test Your Knowledge

Chapter 10

1.  A type of sloping roof that simplifies the construction of an overhang for all outside walls is called a

____________________ roof.

2.  The pitch of a roof is indicated by a fraction formed by placing the rise over the

___________________ .

3.  The tongue of a framing square is ____________________ inches long.

4.  When laying out a rafter for a run that includes a odd unit, the ____________________ (full unit, odd unit) is laid out first.

5.  The bird’s mouth is formed by a(n) ____________________ cut and plumb cut.

6.  The final step in laying out a common rafter is to shorten it at the ____________________ .

7.  When assembling a roof frame, joints in the ridge should occur at the ____________________ of a rafter.

8.  The part of a gable roof that extends beyond the end wall is called the ____________________ .

9.  Referring to a chart, Figure 10-13, used with a super square, give the length of a common rafter and a hip rafter when the run is 14’.

10.  Figures used to make side cuts for hip and valley rafters are found in the ____________________ line of the rafter table on the framing square.

11.  Hip jack rafters have the same tail and overhang as ____________________ rafters.

12.  Jack rafters should be erected in ____________________ to keep the hip or valley rafters straight.

13.  Horizontal ties between rafters on opposite sides of the ridge and usually located in the upper half of

the frame are called ____________________ .

14.  The two general types of dormers are ____________________ and gable.

15.  In residential construction, the gambrel roof is usually framed with a ____________________ located where the two surfaces of different slopes are joined together.

16.  The adjustment in the lower chord of a roof truss to compensate for sag is called _______________ .

17.  The sheathing on a roof frame provides a nailing base for shingles and also adds _______________ .

18.  End joints in the sheathing boards can be made between rafters when ____________________ lumber is used.

19.  The thickness of plywood required for a sheathing application will vary for different roofing

materials and different ____________________ .

20.  To calculate the area of a plain gable roof, multiply the length of the ridge by the length of

a(n)

____________________ .

21.  Explain how to fabricate steel roof trusses on-site.

22.  How is sheathing fastened to steel roof trusses?